## Slide 1: LF Wakeup Receiver AS3933
Oluf Alminde
19 January 2015

## Slide 2: LF Wakeup Receiver
Active RFID tags
  Container tracking
Real-time location systems in buildings
  Persons
  Valuable goods/equipment
Operator identification
  Industrial machines
  Various vehicles
  Computers
Access control
  Hospitals
  handicapped
  Elderly
Wireless sensor networks
  Outdoor monitoring
  Machine monitoring
  Health monitoring
Markets & Applications

## Slide 3: LF Wakeup Receiver
Overview
Device | Sensitivity | Frequency Range | Correlation Bits | Receiver Inputs | Antenna Tuning | Average Current Consumption
AS3930 | 100µVRMS | 100 – 150 kHz | 16 bit | 1D | No | 2.7 µA
AS3932 | 100µVRMS | 100 – 150 kHz | 16 bit | 3D | No | 2.7 µA
AS3933 | 80µVRMS | 15 – 150 kHz | 32 bit | 3D | Yes | 2.7 µA
Best-in-class sensitivity
Lowest power consumptions
Widest frequency range

## Slide 4: LF Wakeup Receiver
Typical system with wakeup
Active Tag with AS3933
Host system and active tag with LF wakeup
UHF Transceiver with LF Wakeup Transmitter
Typical system with LF wakeup
The host system with a transceiver (typically UHF) includes a LF wakeup transmitter
The active tag includes the AS3933 wakeup receiver
Typical wakeup range is up to 10 meters
LF wakeup frequency is programmable from 15 kHz to 150 kHz
Magnetic Coupling
LF signal with wakeup pattern

## Slide 5: LF Wakeup Receiver
Typical active tag
AS3933
Wakeup Receiver
3D
ANTENNA
Host
MCU
SPI
Active Tag
15 … 150 kHz
UHF Transceiver
Typical active tag
Main function is to wake up the host system
The LF antenna coils consist of 3 axis (x/y/z)
AS3933 provides automatic antenna tuning

## Slide 6: LF Wakeup Receiver
Automatic antenna tuning
  Best performance of the solution
  Simplifies antenna matching network
Best sensitivity in the industry
  Maximum communication range
  Allows usage of cheaper antenna coils
Widest frequency range
  More flexibility
  Allows usage of LF frequency outside the conventional range (125 and 134 kHz)
  Less disturbers
32-bit pattern detection
  Very resistant to false wakeup events
  Reduces overall power consumption of the system
Key Features & Benefits

## Slide 7: Thank you
Please visit our website www.ams.com

## Slide 8: AS3933 – LF Wakeup Receiver
Benefits
  Wide frequency range allows for customization
  High sensitivity = longer range, cheaper coils
  Automatic antenna tuning alleviates miss-tuning
  Low power consumption = extended battery life
  Programmable capabilities = system flexibility
Key features
  1, 2 or 3-channal ASK wake-up Rx
  Frequency range: 15-150 kHz
  Best in class wakeup sensitivity: 80µVRMS
  Automatic antenna tuning
  Low current consumption: 2.7 µA
  16- or 32-bit correlation
  TSSOP16 & QFN16
Applications
  Active RFID tags
  Real-time location systems
  Wireless sensors
  ID systems (operator, access control)
  Asset tracking in harsh & wet applications